## Slide 1: TSBB15 3D Reconstruction Group 2 “Epipolarna”

## Slide 2: Modules
Main program and pipeline – Mattias
2D correspondence extraction – Alexander
Non-linear optimization – Martin
Visualization – Gustav

## Slide 3: The 3D Reconstruction pipeline
Noisy, lots of false positives.
False positives are mostly isolated.
Easy to handle with later processing steps.

## Slide 4: Data Structures
Data structure for cameras.
Links original 2D points to 3D points.
Links camera to visible points.

## Slide 5: File output
Output each step of the reconstruction to a file.
Can be read by the visualizer for debugging/demonstration.
Or resume the reconstruction from a previous step.

## Slide 6: 2D point extraction
Find feature points, using Harris response
  Minimum relative quality
  Minimum distance
Calculate descriptor, using SIFT
Calculate correspondences, using Brute Force

## Slide 7: Feature Points

## Slide 8: Corresponding Points

## Slide 9: Initial Pose
Initial relation between cameras is calculated from the essential matrix, according to algorithm described in an epic compendium by Klas Nordberg.
Algorithm used as initial guess for PnP

## Slide 10: Non-linear optimization
Gold Standard estimation of F
PnP pose estimation
Bundle adjustment
Minimizes re-projection error over specified parameters.

## Slide 11: Solving the PnP
Initial guess derived from F
Rotation parameterization
  Rotation vector representation
  Allows for unconstrained optimization
  Ambiguity in the mapping from matrix to parameter vector

## Slide 12: Bundle Adjustment
Minimize total re-projection error
Implemented using levmar
Slow because of
  No sparse pattern for Jacobian estimation
  Library was not build using LAPACK

## Slide 13: Visualization
Plot the estimated cameras
Plot the 3D points.
Points colored from original image data.

## Slide 14: Evaluation
  Slow, especially bundle adjustment step.
  Very good results though.
  Sensitive to outliers.

## Slide 15: Results
Very slow for many cameras.
But it works.
It is awsome.