## Slide 1: TSBB15 3D Reconstruction Group 2 “Epipolarna”

## Slide 2: Modules
Main program and pipeline – Mattias
2D correspondence extraction – Alexander
Non-linear optimization – Martin
Visualization – Gustav

## Slide 3: The 3D Reconstruction pipeline

## Slide 4: Data Structures
Camera data structure
2D <-> 3D
Camera pair & 2D <-> 3D

## Slide 5: Problems
Difficult data set
Outliers
Long time before results are seen

## Slide 6: Improvements
Chains?
1
2
3

## Slide 7: 2D point extraction
Find feature points, using Harris response
  Minimum relative quality
  Minimum distance
Calculate descriptor, using SIFT
Calculate correspondences, using Brute Force

## Slide 8: Feature Points

## Slide 9: Corresponding Points

## Slide 10: Initial Pose
Initial relation between cameras is calculated from the essential matrix, according to algorithm described in an epic compendium by Klas Nordberg.
Algorithm used as initial guess for PnP

## Slide 11: Non-linear optimization
Implemented using the levmar API
Called three times in one pipeline iteration
  Last step of Gold Standard algorithm
  PnP pose estimation
  Bundle adjustment
Minimizes squared re-projection error over specified parameters.

## Slide 12: Rotation parameterization
Vector representation
Support exists in OpenCV: (cv::Rodrigues)
Allows for unconstrained optimization
Ambiguity in the mapping from parameter vector to matrix

## Slide 13: Solving the PnP
Initial guess derived from F (R & t)
Use known correspondences from previous view
Threshold new points on re-projection error to remove outliers

## Slide 14: Bundle Adjustment
Same rotation parameterization as the one used for solving the PnP
Computation time scales badly with the number of points and views
  Dinosaur set takes more than ten hours to complete (30 points per view)
Slow mainly because
  No sparse pattern is used for Jacobian estimation
  levmar was not built using LAPACK

## Slide 15: Visualization
Plot the estimated cameras
Plot the 3D points.
Points colored from original image data.

## Slide 16: Evaluation
  Slow, especially bundle adjustment step.
  Very good results though.
  Sensitive to outliers.

## Slide 17: Results
Very slow for many cameras.
But it works.
It is awsome.